## Slide 1: Smart Cities Architecture and Implementation Workshop: Standards and Technology
Facilitators
Kary Främling
Adjunct Professor
Aalto University,
Finland
Avleen Malhi
Postdoctoral Researcher
Aalto University,
Finland
Tuomas Kinnunen
Research Assistant
Aalto University,
Finland
Asad Javed
PhD Researcher
Aalto University,
Finland
Email: firstname.lastname@aalto.fi

## Slide 2: Agenda
Introduction
Open Messaging Standards (O-MI and O-DF)
O-MI/O-DF Reference Implementation
How to run O-MI node
Live demos
(Scripts and Slides are available at: https://github.com/AaltoAsia/Dublin-workshop)

## Slide 3: Introduction
This workshop will address the practical aspects of using IoT technology to deliver smart city solutions.
Goal of the Workshop:
  Install O-MI Node reference implementation
  Use an IoT device to send sensor values to your Node
  Make a data subscription to send value from your Node to our Node
We will have live visualization of all the data coming to our O-MI Node

## Slide 4: Open Messaging Standards
Defined by The Open Group as Open Messaging Interface (O-MI) and Open Data Format (O-DF)
Provide peer-to-peer communication and real-time interaction between devices or information systems
Capabilities: IoT CRUD (Create, Read, Update, Delete)
O-MI: Provides a framework to publish and consume real-time information
O-DF: Represents a data payload

## Slide 5: Open Data Format (O-DF)
Defined as a simple ontology and specified using XML Schema
Provides structure and mechanism to annotate data for information exchange
Generic enough for representing “any” object and information

## Slide 6: Open Message Interface (O-MI)
Enables communication between heterogeneous devices and information systems
O-MI node can act both as a “server” and as a “client”
O-MI Properties:
  Self-contained messages
  Protocol-agnostic messages
  Different payload formats
  Specifying time-to-live
  Publication and discovery of new services and metadata
  Subscription of data or services
Often used on top of HTTP or Websockets

## Slide 7: O-MI Basic Operations
Write information, such as sensor values, setpoints, alerts, etc
Read current and historical information, alerts, other events
Subscribe to information with or without callback
Cancel subscriptions before expiration

## Slide 8: An example Write message

## Slide 9: O-MI/O-DF Reference Implementation
Open source implementation developed at Aalto University
  Available at: https://github.com/AaltoAsia/O-MI
Enable fast deployment of IoT node

## Slide 10: O-MI Node Server
Main building block of reference implementation
Supports all O-MI operations, handles user requests, and manages the database
Agent management system
  Mechanism to interact programmatically with the core of an O-MI node
  Can filter and modify incoming O-MI requests
  Can push and pull sensor data to and from database

## Slide 11: Web Client
Graphical user interface for the developers to create and test O-MI messages
Sandbox for testing O-MI operations or features

## Slide 12: Wrapper
A piece of code that converts to or from O-MI/O-DF is considered as a “wrapper”
Combine data from different source or system with different/same protocol into single O-DF structure for publishing
Encapsulate underlying lower protocol for data consumer
  e.g. 1-Wire, third party system, KNX etc.
Wrapper can be written in any programming or scripting language.
  e.g.: Shell script, Java, Python, C etc.

## Slide 13: How to run O-MI node?
Dependency Java JDK 1.8
  https://www.oracle.com/technetwork/java/javase/downloads/jdk8-downloads-2133151.html
Run pre-compiled node:
  Download the latest release version and unpack it. Available at: https://github.com/AaltoAsia/O-MI/releases
    For Windows: Use “o-mi-node-1.0.9.zip” (Don’t use deep directory structure)
    For MAC/Linux: Use “o-mi-node-1.0.9.tgz”
  To allow write requests from other machines you need to modify file “<Extracted folder>/conf/application.conf”.
    Change the setting “allowRequestTypesForAll”, add “write” to the list, such that the result looks like this:
    allowRequestTypesForAll = ["read", "cancel", "call", "write"]
  For Windows: Go to the <Extracted folder>/bin and click on o-mi-node.bat For MAC/Linux: cd <Extracted folder>/bin and add execute instructions “chmod +x o-mi-node” and then run “./o-mi-node”
  The server can now be accessed with URL http://localhost:8080/ and open OMI test client on this URL

## Slide 14: Open Firewall port for O-MI in Windows
Navigate to Control Panel -> System and Security -> Windows Firewall
Select ‘Advanced settings’ from the left menu and highlight Inbound Rules in the left pane
Right click Inbound Rules and select New Rule
Select ‘Port’ and click Next
Add the port you need to open and click Next
Select TCP protocol and add ’8080’ in the port field and click Next
Select Allow the connection in the next window and hit Next
Select the network type and click Next
Name the rule something meaningful and click Finish

## Slide 15: O-MI/O-DF Sandbox
Object of Interest
O-MI Operation
O-MI Request
O-MI Response
O-MI Parameters

## Slide 16: Steps to publish data with reference implementation
Step 1: Deploy reference implementation
Step 2: Develop wrapper for getting and publishing data
Step 3: Send O-MI write request to create or update data periodically using wrapper
Step 4: Use Web Client to test other O-MI/O-DF functionality such as one time read, subscription, delete etc.
Note: Other system can also read/subscribe published data by sending read/subscription request.

## Slide 17: Case Study: Smart Home
O-MI/O-DF Web Client
Wrapper
Data Publisher
O-MI/O-DF Reference
Implementation
Data Analytics
Agent Manager 1
Agent 1
O-MI/O-DF Node Server
Agent 2
O-MI
Write
Request
O-MI
Subscription
O-MI
Response
Monitoring Unit

## Slide 18: Smart Home Scenario Description
Smart Home equipped with
  Temperature and Humidity sensor (SHT-20 and 1-wire)
  CO2 sensor (S-100)
Wrapper to publish smart home data to O-MI node
  Read sensor value
  Translate it to O-DF
  Put it in O-MI Write request
  Send with HTTP POST request
Developer can test the system using web-client
Data consumer (Monitoring unit) might be interested in these sensor values for analyzing the required object values. It can subscribe to the objects of interest

## Slide 19: Hardware and Sensors Provided
Raspberry Pi boards (Model 1 and 3)
ESP8266 WiFi development modules
SHT20 Temperature and humidity sensor
S-100 CO2 sensor
1-Wire temperature and humidity sensor

## Slide 20: Live Demo
Implementation Using Raspberry Pi (RPi)

## Slide 21: 1-Wire Sensor Installation
sudo raspi-config -> Interfacing options
  enable 1-wire
  enable i2c protocol
Add ”i2c-bcm2708” and ”i2c-dev” modules (on separate lines) in /etc/modules
  sudo nano /etc/modules
sudo reboot
Verify that i2c bus is enabled
  sudo i2cdetect –y 1
  You should get a table as result

## Slide 22: OWFS Installation
Firstly install some neccesary and useful packages
  sudo apt-get update
  sudo apt-get install automake autoconf autotools-dev gcc-4.7 libavahi-client-dev libtool libusb-dev libusb-1.0-0-dev libfuse-dev swig python2.7-dev i2c-tools
Download the latest version of OWFS
  cd /usr/src
  sudo wget -O owfs-latest.tgz http://sourceforge.net/projects/owfs/files/latest/download
Unpack OWFS
  sudo tar xzvf owfs-3.0p0.tgz
Go to the directory and configure OWFS
  sudo ./configure

## Slide 23: OWFS Installation
Compile OWFS
  sudo make (sudo make -j 4, if RPi-3)
  sudo make install
Create mountpoint for 1-wire
  sudo mkdir /mnt/1wire
To access the 1-wire without root privileges:
  sudo nano /etc/fuse.conf
  Change #user_allow_other to user_allow_other

## Slide 24: Connecting to Raspberry Pi with SSH
Connect to our WiFi “TP-LINK_C5E618”
For Windows:
  Use putty (https://www.putty.org/)
For MAC: Open terminal
Connect to RPi:
  ssh pi@ipAddress
ssh (to RPi-3)
  User: pi
  Password: Qwerty123
ssh (to RPi-1)
  User: pi
  Password: raspberry
Download the provided scripts from https://github.com/AaltoAsia/Dublin-workshop
RPi ID | IP address
R1 | 192.168.1.10
R2 | 192.168.1.11
R3 | 192.168.1.12
R4 | 192.168.1.13
R5 | 192.168.1.14
M1 | 192.168.1.15
W1 | 192.168.1.17
W2 | 192.168.1.16

## Slide 25: Start 1-wire (Start from here with RPi)
Start OWFS
  sudo /opt/owfs/bin/owfs -u /dev/ttyUSB0 --allow_other /mnt/1wire/
Check the contents of 1-wire
  ls /mnt/1wire/
  (You will find the directory starting with 26. which contains the sensors data (or 2 directories with 26. if using two 1-wire sensors in chain))
Read the sensor values from the directory starting with ”26.”
  cat /mnt/1wire/<26…>/temperature
  cat /mnt/1wire/<26…>/humidity
Download the scripts on Raspberry Pi and go to the cloned directory:
    git clone https://github.com/AaltoAsia/Dublin-workshop.git
    cd Dublin-workshop

## Slide 26: Start 1-wire
‘omi-write.sh’ and ‘create-odf.sh’ scripts on GitHub is used to send 1-wire data to O-MI node
In the “create-odf.sh” script:
  Type “nano create-odf.sh” to edit this script file
  Update the Object id to some unique name. Change the name ‘OneWireSensor’ (appeared in two places) to your own defined name.
  Update the 1-wire sensor id in the following line:
Place sensor id here starting with 26.

## Slide 27: Start 1-wire
Find the IP address of your laptop (where you run O-MI node):
  For Mac/Linux: Run “ifconfig” in the terminal and note the IP address of wlan0 interface:
  For Windows: Run “ipconfig” in the command prompt.
In the “omi-write.sh” script:
  Change the address of O-MI node to http://yourIP:8080 in the following line at the end of script:
    “curl_cmd=$(curl --data "$(omiWrite)" "http://myhost:port")”
Finally, run the script
  ./omi-write.sh

## Slide 28: Raspberry Pi Pinout
Raspberry Pi 1
Raspberry Pi 3

## Slide 29: CO2 Sensor (Model: S-100)
5V
GND
TX
Connect jumper cables:
  Sensor TX -> RPi RX
  Sensor GND -> RPi GND
  Sensor 5V -> RPi 5V
Run ‘./co2-omi-send.py’ script

## Slide 30: Temperature and Humidity Sensor (Model: SHT-20)
# ? * ?
+ GND * ?
*? * 3v3
*? * SDC
*? * SDA
GND
3.3V
SDC
SDA

## Slide 31: Temperature and Humidity Sensor (Model: SHT-20)
Install the sensor python library
  sudo apt-get update
  sudo pip3 install sensor
Connect the jumper cables:
  Sensor SDC -> RPi SDC
  Sensor SDA -> RPi SDA
  Sensor GND -> RPi GND
  Sensor 3V -> RPi 3V
Read the temperature and humidity value (run the provided python script ’./ht-omi-send.py’ or ’python3 ht-omi-send.py’)
Important steps:
  Do change the address of O-MI node (http://yourIP:8080)
  Also, please change the Object id to some unique name in the O-MI XML structure

## Slide 32: Live Demo
Implementation Using ESP8266

## Slide 33: ESP8266 Arduino Configuration
The ESP8266 is a very low-cost Wi-Fi microchip with full TCP/IP stack and microcontroller capability.
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
  Install latest Arduino IDE from https://www.arduino.cc/en/main/software
  Start Arduino and open Preferences window.
  Enter https://arduino.esp8266.com/stable/package_esp8266com_index.json into Additional Board Manager URLs field.
  Open Boards Manager from Tools > Board menu and install esp8266 platform
  For MAC machine, download and install the driver ”CH34x_Install_V1.5.pkg” from https://github.com/adrianmihalko/ch340g-ch34g-ch34x-mac-os-x-driver
  Restart the Arduino IDE

## Slide 34: CO2 Sensor (Model: S-100)
5V
GND
TX
Connect jumper cables:
  Sensor TX -> ESP RX
  Sensor GND -> ESP GND
  Sensor 5V -> ESP 5V

## Slide 35: Interfacing CO2 Sensor with ESP8266
Connect ESP chip with your laptop USB port.
Start Arduino IDE and select the following board from Tools -> Board
  LOLIN (WEMOS) D1 R2 and Mini
Select port using Tools -> Port
Open /SoS-Scripts/CO2_test (test scripts for CO2 sensor)
Open create_odf tab in Arduino and change <id> of the Object to something unique and change the url to your O-MI Node (http://yourIP:8080/)
Note: Disconnect the RX of ESP8266 while uploading the code.
Press Upload button
Connect RX of ESP8266 again after uploading is done.
If it fails you might have wrong port or too high upload speed
View the output through Tools -> Serial Monitor
  Select baud rate as 38400

## Slide 36: Temperature and Humidity Sensor (Model: SHT-20)
# ? * ?
+ GND * ?
*? * 3v3
*? * SDC
*? * SDA
GND
3.3V
SDC
SDA
Connect jumper cables:
  Sensor SDA -> ESP SDA (D2)
  Sensor SDC -> ESP SDL (D1)
  Sensor GND -> ESP GND
  Sensor 3.3V -> ESP 3V3

## Slide 37: SHT20 Sensor
Download the library for SHT20 from https://github.com/DFRobot/DFRobot_SHT20 into the ’libraries’ folder of your Arduino installation directory (<....>/Documents/Arduino/libraries).
Open /SoS-Scripts/temp_humi_test (test scripts for SHT20 sensor)
Open create_odf tab in Arduino and change <id> of the Object to something unique and change the url to your O-MI Node (http://yourIP:8080/)
Press Upload button
Tools -> Serial Monitor
  Select baud rate as 115200

## Slide 38: CPU Temperature (For Linux machine)
Install some required packages
  sudo apt-get update
  sudo apt-get install lm-sensors
  sudo sensors-detect
Start the service
  sudo service kmod start
Read the temperature and send the value to O-MI node using the provided script.
  while true; do sensors -u | awk '/temp1_input/ {print $2}' | ./omi-send-linux.py; sleep 2s; done

## Slide 39: CPU Temperature (For MAC machine)
Download latest version of python: (if not already installed) https://www.python.org/downloads/release/python-373/
Download pip for python3 and other required packages:
  curl https://bootstrap.pypa.io/get-pip.py -o get-pip.py
  python3 get-pip.py
  pip3 install requests
Reading CPU Temperature
  Download source code from https://github.com/lavoiesl/osx-cpu-temp
  Unzip the downloaded folder and ’cd’ to that directory
  Run make
  Copy omi-send-mac.py to the same directory
  while true; do ./osx-cpu-temp | ./omi-send-mac.py; sleep 2s; done

## Slide 40: Create a subscription for our visualization Node
Go to http://localhost:8080/ and go to ”O-MI Test Client WebApp”
Check that your data have been received correctly with a Read request, after that, continue with subscription:
Select ”Objects” from the O-DF tree
Select ”Subscription” request
Open ”Optional parameters”
Put address of the visualization node (http://192.168.1.20:8080/) to ”callback” field
Press ”Send” and see if your value shows on the visualization (after it changes next time)

## Slide 41
Questions

## Slide 42
Extra slides

## Slide 43: Interoperability
Interoperability Challenge
  Communication Interoperability
    Infrastructure and mechanism
    Technology Level
      e.g. TCP/IP
    Interface Level
      Means of communication
      e.g. O-MI, HTTP
  Data Level Interoperability
    Syntactic Level
      Common Data Format
      e.g. O-DF, CSV
    Semantic Level
      Shared Meaning
      e.g. Mobivoc

## Slide 44: Raspberry Pi setup
Operating System Installation:
Download and unzip Soft-float Debian “Wheezy" Operating System for Raspberry pi from http://www.raspberrypi.org/downloads
For flashing the Wheezy Operating System in SD card of the Raspberry Pi download and unzip Win32DiskImager.exe from http://sourceforge.net/projects/win32diskimager/
Run Win32DiskImager.exe , select the .img file unzipped from step 1, select the SD card and click Write.
Eject SD card safely from writer and insert it into raspberry.
Insert SD card in raspberry PI and connect the necessary IO devices (mouse, Keyboard and monitor) and Internet cable. start it by supplying the power.

## Slide 45: Java Installation
Login into raspberry pi using default credential (username=pi and password= raspberry)
sudo apt-get update
sudo apt-get install openjdk-7-jdk

## Slide 46: Writing data to O-MI Node
Add the sensor objects while creating data format
Add the IP address of the receiver O-MI node in write message
(The scripts have been created for your reference)
# Send write message
#curl_cmd=$(curl --data "$(omiWrite)" "http://192.168.1.100:8080")
Object="OneWireSensor"
OneWireSensor_Object="Sensor1"
Sensor1_InfoItems="Temperature Humidity"
Sensor1_values="`eval "cat /mnt/1wire/26.0F85CB010000/temperature"` `eval "cat /mnt/1wire/26.0F85CB010000/humidity"`"

## Slide 47: CO2 Sensor (Model: S-100)
Getting the value of sensor (baud speed is 38400)
Add the IP address of the receiver O-MI Node in OMI Node write script
(The script for sending the data has already been created for your reference)
Sending the value to O-MI Node
miniterm.py /dev/serial0 38400
miniterm.py /dev/serial0 38400 | ./omi-sent.py
miniterm.py /dev/ttyS0 38400
miniterm.py /dev/ttyS0 38400 | ./omi-sent.py
requests.post("http://192.168.1.103:8080"
Raspberry Pi 1
Raspberry Pi 3
Raspberry Pi 1
Raspberry Pi 3