## Slide 1: Smart Cities Architecture and Implementation Workshop: Standards and Technology
Facilitators
Kary Främling
Adjunct Professor
Aalto University,
Finland
Avleen Malhi
Postdoctoral Researcher
Aalto University,
Finland
Tuomas Kinnunen
Research Assistant
Aalto University,
Finland
Asad Javed
PhD Researcher
Aalto University,
Finland
Email: firstname.lastname@aalto.fi

## Slide 2: Agenda
Introduction
Open Messaging Standards (O-MI and O-DF)
O-MI/O-DF Reference Implementation
How to run O-MI node
Live demos
(Scripts and Slides are available at: https://github.com/AaltoAsia/Dublin-workshop)

## Slide 3: Introduction
This workshop will address the practical aspects of using IoT technology to deliver smart city solutions.
Goal of the Workshop:
  Install O-MI Node reference implementation
  Use an IoT device to send sensor values to your Node
  Make a data subscription to send value from your Node to our Node
We will have live visualization of all the data coming to our O-MI Node

## Slide 4: Open Messaging Standards
Defined by The Open Group as Open Messaging Interface (O-MI) and Open Data Format (O-DF)
Provide peer-to-peer communication and real-time interaction between devices or information systems
Capabilities: IoT CRUD (Create, Read, Update, Delete)
O-MI: Provides a framework to publish and consume real-time information
O-DF: Represents a data payload

## Slide 5: Open Data Format (O-DF)
Defined as a simple ontology and specified using XML Schema
Provides structure and mechanism to annotate data for information exchange
Generic enough for representing “any” object and information

## Slide 6: Open Message Interface (O-MI)
Enables communication between heterogeneous devices and information systems
O-MI node can act both as a “server” and as a “client”
O-MI Properties:
  Self-contained messages
  Protocol-agnostic messages
  Different payload formats
  Specifying time-to-live
  Publication and discovery of new services and metadata
  Subscription of data or services
Often used on top of HTTP or Websockets

## Slide 7: O-MI Basic Operations
Write information, such as sensor values, setpoints, alerts, etc
Read current and historical information, alerts, other events
Subscribe to information with or without callback
Cancel subscriptions before expiration

## Slide 8: An example Write message

## Slide 9: O-MI/O-DF Reference Implementation
Open source implementation developed at Aalto University
  Available at: https://github.com/AaltoAsia/O-MI
Enable fast deployment of IoT node

## Slide 10: O-MI Node Server
Main building block of reference implementation
Supports all O-MI operations, handles user requests, and manages the database
Agent management system
  Mechanism to interact programmatically with the core of an O-MI node
  Can filter and modify incoming O-MI requests
  Can push and pull sensor data to and from database

## Slide 11: Web Client
Graphical user interface for the developers to create and test O-MI messages
Sandbox for testing O-MI operations or features

## Slide 12: Wrapper
A piece of code that converts to or from O-MI/O-DF is considered as a “wrapper”
Combine data from different source or system with different/same protocol into single O-DF structure for publishing
Encapsulate underlying lower protocol for data consumer
  e.g. 1-Wire, third party system, KNX etc.
Wrapper can be written in any programming or scripting language.
  e.g.: Shell script, Java, Python, C etc.

## Slide 13: How to run O-MI node?
Dependency Java 1.8 (https://www.java.com/en/download/)
Run pre-compiled node:
  Download the latest release version (.zip/.tar) and unpack it. Available: https://github.com/AaltoAsia/O-MI/releases
  Go to the <Extracted folder>/bin and run o-mi-node.bat (for Windows) or o-mi-node (for Unix/Mac)
  The server can now be accessed with URL http://localhost:8080/
  To allow write requests from other machines you need to modify file “<Extracted folder>/conf/ application.conf”.
    Change the setting “allowRequestTypesForAll”, add “write” to the list, such that the result looks like this:
    allowRequestTypesForAll = ["read", "cancel", "call", "write"]
  Restart the O-MI Node
If you want to compile from source code: Follow instructions on the Github Readme

## Slide 14: O-MI/O-DF Sandbox
Object of Interest
O-MI Operation
O-MI Request
O-MI Response
O-MI Parameters

## Slide 15: Steps to publish data with reference implementation
Step 1: Deploy reference implementation
Step 2: Develop wrapper for getting and publishing data
Step 3: Send O-MI write request to create or update data periodically using wrapper
Step 4: Use Web Client to test other O-MI/O-DF functionality such as one time read, subscription, delete etc.
Note: Other system can also read/subscribe published data by sending read/subscription request.

## Slide 16: Case Study: Smart Home
O-MI/O-DF Web Client
Wrapper
Data Publisher
O-MI/O-DF Reference
Implementation
Data Analytics
Agent Manager 1
Agent 1
O-MI/O-DF Node Server
Agent 2
O-MI
Write
Request
O-MI
Subscription
O-MI
Response
Monitoring Unit

## Slide 17: Smart Home Scenario Description
Smart Home equipped with
  Temperature and Humidity sensor (SHT-20 and 1-wire)
  CO2 sensor (S-100)
Wrapper to publish smart home data to O-MI node
  Read sensor value
  Translate it to O-DF
  Put it in O-MI Write request
  Send with HTTP POST request
Developer can test the system using web-client
Data consumer (Monitoring unit) might be interested in these sensor values for analyzing the required object values. It can subscribe to the objects of interest

## Slide 18: Hardware and Sensors Provided
Raspberry Pi boards (Model 1 and 3)
ESP8266 WiFi development modules
SHT20 Temperature and humidity sensor
S-100 CO2 sensor
1-Wire temperature and humidity sensor

## Slide 19: Live Demo
Implementation Using Raspberry Pi (RPi)

## Slide 20: 1-Wire Sensor Installation
sudo raspi-config -> Interfacing options
  enable 1-wire
  enable i2c protocol
Add ”i2c-bcm2708” and ”i2c-dev” modules (on separate lines) in /etc/modules
  sudo nano /etc/modules
sudo reboot
Verify that i2c bus is enabled
  sudo i2cdetect –y 1
  You should get a table as result

## Slide 21: OWFS Installation
Firstly install some neccesary and useful packages
  sudo apt-get update
  sudo apt-get install automake autoconf autotools-dev gcc-4.7 libavahi-client-dev libtool libusb-dev libusb-1.0-0-dev libfuse-dev swig python2.7-dev i2c-tools
Download the latest version of OWFS
  cd /usr/src
  sudo wget -O owfs-latest.tgz http://sourceforge.net/projects/owfs/files/latest/download
Unpack OWFS
  sudo tar xzvf owfs-3.0p0.tgz
Go to the directory and configure OWFS
  sudo ./configure

## Slide 22: OWFS Installation
Compile OWFS
  sudo make (sudo make -j 4, if RPi-3)
  sudo make install
Create mountpoint for 1-wire
  sudo mkdir /mnt/1wire
To access the 1-wire without root privileges:
  sudo nano /etc/fuse.conf
  Change #user_allow_other to user_allow_other

## Slide 23: Connecting to Raspberry Pi with SSH
Connect to our WiFi “TP-LINK_C5E618”
For Windows:
  Use putty (https://www.putty.org/)
Connect to RPi:
  ssh pi@ipAddress
ssh (to RPi-3)
  User: pi
  Password: Qwerty123
ssh (to RPi-1)
  User: pi
  Password: raspberry
RPi ID | IP address
R1 | 192.168.1.10
R2 | 192.168.1.11
R3 | 192.168.1.12
R4 | 192.168.1.13
R5 | 192.168.1.14
M1 | 192.168.1.15
W1 | 192.168.1.17
W2 | 192.168.1.16

## Slide 24: Start 1-wire (Start from here with RPi)
Start OWFS
  sudo /opt/owfs/bin/owfs -u /dev/ttyUSB0 --allow_other /mnt/1wire/
Check the contents of 1-wire
  ls /mnt/1wire/
  (You will find the directory starting with 26. which contains the sensors data (or 2 directories with 26. if using two 1-wire sensors in chain))
Read the sensor values from the directory starting with ”26.”
‘omi-write.sh’ and ‘create-odf.sh’ scripts on GitHub is used to send 1-wire data to O-MI node
Important steps:
  Do change the sensor directory name in create-odf.sh script
  Also, please change the Object id to some unique name in the O-MI XML structure

## Slide 25: Raspberry Pi Pinout
Raspberry Pi 1
Raspberry Pi 3

## Slide 26: CO2 Sensor (Model: S-100)
5V
GND
TX
Connect jumper cables:
  Sensor TX -> RPi RX
  Sensor GND -> RPi GND
  Sensor 5V -> RPi 5V
Run ‘./co2-omi-send.py’ script

## Slide 27: Temperature and Humidity Sensor (Model: SHT-20)
# ? * ?
+ GND * ?
*? * 3v3
*? * SDC
*? * SDA
GND
3.3V
SDC
SDA

## Slide 28: Temperature and Humidity Sensor (Model: SHT-20)
Install the sensor python library
  sudo apt-get update
  sudo pip3 install sensor
Connect the jumper cables:
  Sensor SDC -> RPi SDC
  Sensor SDA -> RPi SDA
  Sensor GND -> RPi GND
  Sensor 3V -> RPi 3V
Read the temperature and humidity value (run the provided python script ’./ht-omi-send.py’ or ’python3 ht-omi-send.py’)
Important steps:
  Do change the address of O-MI node (http://yourIP:8080)
  Also, please change the Object id to some unique name in the O-MI XML structure

## Slide 29: Live Demo
Implementation Using ESP8266

## Slide 30: ESP8266 Arduino Configuration
The ESP8266 is a very low-cost Wi-Fi microchip with full TCP/IP stack and microcontroller capability.
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
Follow the instructions on the link (https://github.com/esp8266/Arduino) to download Arduino and ESP core
Start Arduino IDE and select the following board from Tools -> Board
  LOLIN (WEMOS) D1 R2 and Mini
On MAC you might need a driver:
  https://github.com/adrianmihalko/ch340g-ch34g-ch34x-mac-os-x-driver

## Slide 31: ESP8266 Arduino Configuration
Select port using Tools -> Port
Open the required script
Open create_odf tab and change <id> of the Object to something unique and change the url to your O-MI Node (http://yourIP:8080/), also make sure that both devices are on same wifi network
Press Upload button
If it fails you might have wrong port or too high upload speed
View the output through Tools -> Serial Monitor

## Slide 32: SHT-20 Sensor
Download the library for SHT20 from the given link
  https://github.com/DFRobot/DFRobot_SHT20
Use Jumper cables to connect the required sensor ports (SDA, SDC, Voltage, and GND)
Use the provided code in the folder ’temp_humi_test’
Add the IP address of the receiving O-MI node and change the name of O-DF Object id in the code
Tools -> Serial Monitor
  Select baud rate as 115200

## Slide 33: S-100 Sensor
Add the IP address of the receiving O-MI node and change the name of O-DF Object id in the code
Connect TX of S-100 with RX of ESP8266.
Upload the code on ESP8266
Note: Disconnect the RX of ESP8266 while uploading the code and connect it again after the uploading is done.
Tools -> Serial Monitor
  Select baud rate as 38400

## Slide 34: CPU Temperature (For Linux machine)
Install some required packages
  sudo apt-get update
  sudo apt-get install lm-sensors
  sudo sensors-detect
Start the service
  sudo service kmod start
Read the temperature and send the value to O-MI node using the provided script.
  while true; do sensors -u | awk '/temp1_input/ {print $2}' | ./omi-send-linux.py; sleep 2s; done

## Slide 35: CPU Temperature (For MAC machine)
Download latest version of python: (if not already installed) https://www.python.org/downloads/release/python-373/
Download pip for python3 and other required packages:
  curl https://bootstrap.pypa.io/get-pip.py -o get-pip.py
  python3 get-pip.py
  pip3 install requests
Reading CPU Temperature
  Download source code from https://github.com/lavoiesl/osx-cpu-temp
  Unzip the downloaded folder and ’cd’ to that directory
  Run make
  Copy omi-send-mac.py to the same directory
  while true; do ./osx-cpu-temp | ./omi-send-mac.py; sleep 2s; done

## Slide 36: Create a subscription for our visualization Node
Go to http://localhost:8080/ and go to ”O-MI Test Client WebApp”
Check that your data have been received correctly with a Read request, after that, continue with subscription:
Select ”Objects” from the O-DF tree
Select ”Subscription” request
Open ”Optional parameters”
Put address of the visualization node to ”callback” field
Press ”Send” and see if your value shows on the visualization (after it changes next time)

## Slide 37
Questions

## Slide 38
Extra slides

## Slide 39: Interoperability
Interoperability Challenge
  Communication Interoperability
    Infrastructure and mechanism
    Technology Level
      e.g. TCP/IP
    Interface Level
      Means of communication
      e.g. O-MI, HTTP
  Data Level Interoperability
    Syntactic Level
      Common Data Format
      e.g. O-DF, CSV
    Semantic Level
      Shared Meaning
      e.g. Mobivoc

## Slide 40: Raspberry Pi setup
Operating System Installation:
Download and unzip Soft-float Debian “Wheezy" Operating System for Raspberry pi from http://www.raspberrypi.org/downloads
For flashing the Wheezy Operating System in SD card of the Raspberry Pi download and unzip Win32DiskImager.exe from http://sourceforge.net/projects/win32diskimager/
Run Win32DiskImager.exe , select the .img file unzipped from step 1, select the SD card and click Write.
Eject SD card safely from writer and insert it into raspberry.
Insert SD card in raspberry PI and connect the necessary IO devices (mouse, Keyboard and monitor) and Internet cable. start it by supplying the power.

## Slide 41: Java Installation
Login into raspberry pi using default credential (username=pi and password= raspberry)
sudo apt-get update
sudo apt-get install openjdk-7-jdk

## Slide 42: Writing data to O-MI Node
Add the sensor objects while creating data format
Add the IP address of the receiver O-MI node in write message
(The scripts have been created for your reference)
# Send write message
#curl_cmd=$(curl --data "$(omiWrite)" "http://192.168.1.100:8080")
Object="OneWireSensor"
OneWireSensor_Object="Sensor1"
Sensor1_InfoItems="Temperature Humidity"
Sensor1_values="`eval "cat /mnt/1wire/26.0F85CB010000/temperature"` `eval "cat /mnt/1wire/26.0F85CB010000/humidity"`"

## Slide 43: CO2 Sensor (Model: S-100)
Getting the value of sensor (baud speed is 38400)
Add the IP address of the receiver O-MI Node in OMI Node write script
(The script for sending the data has already been created for your reference)
Sending the value to O-MI Node
miniterm.py /dev/serial0 38400
miniterm.py /dev/serial0 38400 | ./omi-sent.py
miniterm.py /dev/ttyS0 38400
miniterm.py /dev/ttyS0 38400 | ./omi-sent.py
requests.post("http://192.168.1.103:8080"
Raspberry Pi 1
Raspberry Pi 3
Raspberry Pi 1
Raspberry Pi 3